## Slide 1: ECE477 Midterm Design Review: Team #20
Brian Dye Nate Shenk Henry Wang Hanyu Zhu

## Slide 2: Outline
Project Overview
Major Components
Block Diagram
Packaging Design
Electrical Schematic
PCB Layout
Prototyping Progress
Software Development Status
Project Timeline
Questions

## Slide 3: Project Overview
Enigma is a Mobile Ad-Hoc Network
Each node in the network is simultaneously a host and router
Goal is to provide digital communication services without pre-existing infrastructure
Enigma will be service mobile devices such as a phone or a laptop
The network is dynamic, self-forming, and self-organizing

## Slide 4: PSSCs
An ability to interface RFM69HCW module with STM32 via SPI
An ability to interface SAM-M8Q with STM32 via I2C
An ability to interface a Bluetooth module with STM32 via USART
An ability to route packets under dynamically changing geographic locations
An ability to send a message from the application on one end-device (i.e. a phone connected to a node via BLE) to another end-device

## Slide 5: Major Components
The STM32F0 is a microcontroller with SPI, USART, and I2C serial protocols
48 MHz 32-bit CPU and is suited for cost-sensitive embedded applications
Utilizes the open sourced FreeRTOS
256 KB Flash, 32 KB SRAM
Microcontroller: STM32F091RCT6

## Slide 6: Major Components
The RFM69HCW is a radio module used to send and receive data through short-range, wireless networks
Offers low power and short-medium range transmission
Max bitrate of 300 kbps and frequency band of 915 MHz
Offers a range of up to 500 meters (outdoors)
Operating conditions: 3.3 V @ ~95mA
Radio Module: RFM69HCW

## Slide 7: Major Components
The HM-19 interfaces a node in the network with a Bluetooth compatible device
Operating conditions: 3.3V @ 3.6 mA
Offers a transmit power of 3 dBm
Baud rate: 9600
Bluetooth Module: HM-19

## Slide 8: Major Components
The SAM-MQ8 is a u-blox GNSS patch antenna module with GPS capabilities
Is UART, USB, SPI, and I2C compliant
Has a horizontal accuracy of 2.5 meters
Offers a max update rate of 10 MHz
Will be used to display the coordinates of individual node on LCD screen
GPS Module: SAM-M8Q

## Slide 9: Major Components
The S9V11F3S5C3 is a voltage regulator which takes input voltage ranging from 2 V to 16 V and produces a fixed output voltage of either 3.3 V or 5 V
Has a 3 V low voltage cutoff
Increases or decreases the produced fixed voltage depending on if input voltage is higher or less than 3 V or 16 V
Can be programmed to return an output voltage or 3.3 V or 5 V if set
Will be used to regulate our output voltage
Voltage Regulator: S9V11F3S5C3

## Slide 10: Major Components
The SparkFun Battery Babysitter is a single-cell Lithium Polymer (LiPo) battery manager
Can measure battery voltage to estimate the charge percentage and remaining capacity
Has adjustable charge rate up to 1.5 A
USB-compliant 100 mA and 500 mA options
Will be used to charge our battery as well as monitor the battery
Battery Manager: SparkFun Battery Babysitter

## Slide 11: Block Diagram

## Slide 12: Packaging Design

## Slide 13: Electrical Schematic

## Slide 14: Electrical Schematic: Power

## Slide 15: Electrical Schematic: STM32

## Slide 16: Electrical Schematic: STM32 Decoupling

## Slide 17: Electrical Schematic: HM-19 BLT

## Slide 18: Electrical Schematic: LCD Screen

## Slide 19: Electrical Schematic: SAM-M8Q

## Slide 20: Electrical Schematic: RFM69HCW

## Slide 21: Electrical Schematic: Sparkfun Battery Babysitter

## Slide 22: PCB Layout

## Slide 23
Click to add text
Click to add text
Click to add text
Power Supply block
Microcontroller block
Radio Comm block
GPS module block
Bluetooth module block
GPS reset button
Programming header
Antenna for radio module
LCD Screen
block

## Slide 24: Prototyping Progress: RFM69HCW Radio Module
    Sending and receiving data between two RFM69HCWs has been tested and is working
    Need to configure and utilize module to communicate with other nodes in network

## Slide 25: Prototyping Progress: HM-19 Bluetooth Module
  Bluetooth communication between HM-19 and some laptop or phone has been tested and proven to work
  Need to integrate module with other modules

## Slide 26: Prototyping Progress: SAM-M8Q GPS Module
  Module has not been configured or tested yet
  Need to interface module with STM32 and proven to work

## Slide 27: Prototyping Progress: LCD Screen
  LCD Screen has been fully configured and tested
  Screen display information has been set up and is working
  Need to configure power ON/OFF button

## Slide 28: Software development status: RFM69HCW Radio Module
  Interface RFM69HCW with STM32 (SPI): Completed
  Send and Receive data from one RFM69HCW to another:
  Completed
  Implement dynamic routing protocol:
  In development

## Slide 29: Software development status: UI APPLICATION
  Progressive web application to send texts from one node to another: In development
  Map view showing locations of active nodes in network: In development

## Slide 30: Software development status: HM-19 Bluetooth Module
  Interface HM-19 with STM32 (USART): Completed
  Send data from application to STM-32 via HM-19: Completed
  Automate transfer of information from application to STM-32: In development

## Slide 31: Software development status: SAM-M8Q GPS Module
  Interface SAM-M8Q with STM32 (I2C): In development

## Slide 32: Software development status: MP-2202 LCD Screen
  Interface LCD Screen with STM32 (SPI): Completed
  Update screen with relevant information: In development
  Button interrupt for screen to save battery life: In development

## Slide 33: Project Timeline
Week 8: Setup I2C interface with GPS and Battery Baby Sitter
Week 9: Order PCB
Week 10: Spring Break
Week 11: Routing Protocol Design and UI Application
Week 12: Routing Protocol Design and UI Application
Week 13: Real-Time Scheduling and UI Application
Week 14: Real-Time Scheduling and UI Application
Week 15: Tweak and Finalize
Week 16: Demonstration

## Slide 34
Questions?